## Slide 1
MSC MATHEMATICAL ENGINEERING · A.Y. 2025/26
Verification and validation
of fluid flows
Numerical analysis of internal flows
and experimental characterisation of a circular-cylinder wake
Antonio Arbizzani Tonelli

## Slide 2
OVERVIEW
02
Project at a glance
Numerical and experimental study of two canonical flows, organised as a verification and validation chain. Every reported quantity is tied to a reference solution or measurement, and an explicit error metric.
LAMINAR PIPE · VERIFICATION
1.24%
Pressure-gradient error against Hagen–Poiseuille; profile error 3.18%
TURBULENT PIPE · VALIDATION
0.082%
Friction-factor error of standard k– ε at Reb = 75,000
CYLINDER WAKE · SHEDDING
St 0.18–0.20
Identified independently from PSV velocity and lift force
CYLINDER FORCES · UNCERTAINTY
1.50 ± 0.08
Mean drag coefficient with first-order standard uncertainty
METHODS
RANS CFD (PHOENICS) · grid-sensitivity analysis · particle-shadow velocimetry · spectral analysis · load-cell calibration · uncertainty propagation · MATLAB data processing

## Slide 3
OBJECTIVE
03
Research objective
Establish a traceable verification and validation chain for numerical pipe flow and experimental cylinder-wake measurements.
CASE 1 · INTERNAL FLOW
Pipe flow, CFD
Regimes
Laminar, Reb = 193 · turbulent, Reb = 75,000
Reference
Hagen–Poiseuille solution; measured profiles and friction factor
Test
Verification of the solver, validation of four k–ε closures
Compared
Velocity profile, pressure gradient, Darcy friction factor
CASE 2 · SEPARATED FLOW
Cylinder wake, experiment
Regime
Unsteady wake, ReD ≈ 104
Reference
No closed-form solution: calibrated measurement chain
Test
Characterisation of the wake with quantified uncertainty
Compared
Mean field, Strouhal number, force coefficients

## Slide 4
PROBLEM
04
Verification and validation framework
NUMERICAL · PHOENICS PIPE FLOW
EXPERIMENTAL · FLUME, CIRCULAR CYLINDER
1
Grid sensitivity
Relative profile difference
2
Analytical verification
Poiseuille profile and pressure gradient
3
Model validation
Velocity RMSE and friction factor
4
Measurement calibration
Force residual
5
Wake characterisation and uncertainty
Strouhal number and force coefficients
Verification — does the solver reproduce a known solution?
Validation — does the model reproduce measurements?
Grid sensitivity — necessary, but not proof of physical accuracy.

## Slide 5
PART I
Internal flow CFD
Grid sensitivity, analytical verification of laminar flow, and validation of four k–ε closures against turbulent pipe measurements.
06 Numerical setup
07 Laminar grid
08 Turbulent grid
09 Laminar development
10 Poiseuille profile
11 Pressure gradient
12 Turbulent development
13 Turbulent structure
14 Wall scaling
15 Profile validation
16 Friction factor

## Slide 6
I · INTERNAL FLOW · CFD
06
Numerical setup
Parameter
Laminar
Turbulent
Diameter D
0.15 m
0.10 m
Bulk velocity Wb
0.45 m/s
0.75 m/s
Kinematic viscosity ν
3.5·10−4 m2/s
10−6 m2/s
Reb = WbD/ν
192.9
75,000
Closure
—
4 k–ε models
Axisymmetric pipe solved with PHOENICS. Turbulent closures: standard, RNG, realisable and low-Re k–ε . The comparison is specific to the implemented grids and wall treatments.
Grid sensitivity, successive grids
εi,i+1 = ‖φiint − φi+1‖∞ / ‖φi+1‖∞
Developed flow
εp(z) = ‖W(r,z) − Wref(r)‖∞ / ‖Wref‖∞ ≤ 10−3
Darcy friction factor
f = 8τw / (ρWb2)
Profile validation
Normalised RMSE on experimental radial coordinates

## Slide 7
I · INTERNAL FLOW · CFD
07
Laminar grid: medium–fine differences below 1%
METHOD
Three grids per path. Radial and combined: velocity profile at z ≈ 0.8L . Axial: pressure at half radius. Coarse result interpolated onto the finer grid.
OBSERVATION
Radial 2.36 → 0.52%, axial 0.41 → 0.23%, combined 1.44 → 0.93%. No change in shape and no spurious oscillations.
IMPLICATION
The finest grid is retained. Pairwise differences, not a formal GCI: the refinement ratio is not uniform across directions.

## Slide 8
I · INTERNAL FLOW · CFD
08
Turbulent grid: lower sensitivity than the laminar case
GRIDS
Radial 10 / 25 / 50 cells, axial 100 / 150 / 200 cells, combined 10×100 → 25×250.
OBSERVATION
Medium–fine differences 0.24% radial, 0.13% axial, 0.37% combined. Residual differences concentrate near the wall.
IMPLICATION
The tested refinements produce small profile changes. Model differences are interpreted for these grids and wall treatments.

## Slide 9
I · INTERNAL FLOW · CFD
09
Laminar entry length depends on its definition
CRITERION
First axial station where the full profile is within 0.1% of the last interior profile.
Correlation 0.0575 Re D
1.663 m
Numerical, 0.1% criterion
2.113 m
OBSERVATION
Centreline velocity tends to 2Wb ; the profile distance decreases monotonically.
IMPLICATION
The 27% gap reflects the strict full-profile threshold and discrete axial sampling. The asymptotic state is correct.

## Slide 10
I · INTERNAL FLOW · CFD
10
Developed profile matches Poiseuille within 3.2%
REFERENCE
W/Wb = 2[1 − (r/R)2]
Profile L∞ error
3.18%
Reconstructed Wb
0.4523 m/s · 0.51%
OBSERVATION
The largest differences occur near the wall, where the computed radial profile is steep.
IMPLICATION
The computed profile agrees closely with Poiseuille flow on the tested mesh. The remaining local error has not been isolated.

## Slide 11
I · INTERNAL FLOW · CFD
11
Pressure gradient matches the analytical value within 1.24%
METHOD
Area-weighted pressure p̄(z) = (2/R2)∫p r dr ; least-squares slope over the developed stations. Reference −32 μWb/D2.
Analytical
−203.84 Pa/m
CFD
−201.32 Pa/m
Error
1.24%
OBSERVATION
Pressure becomes linear once inlet development is complete.
IMPLICATION
The integral momentum balance and the implied wall shear are verified independently of the profile.

## Slide 12
I · INTERNAL FLOW · CFD
12
Turbulent flow: the centreline converges before the profile
Correlation 1.359 D Re1/4
2.249 m
Full-profile 0.1% criterion
9.85 m
OBSERVATION
Centreline velocity stabilises early; the full radial profile keeps changing weakly downstream. Pressure decreases linearly once developed.
IMPLICATION
A turbulent entry length is not unique: it depends on the observable and on the threshold used to define it.

## Slide 13
I · INTERNAL FLOW · CFD
13
Developed turbulent field: flat core, active wall region
FIELDS
Mean velocity, eddy-viscosity ratio νt/ν, turbulent kinetic energy k and dissipation ε in the developed region, standard k–ε.
OBSERVATION
The mean profile is flatter than the laminar parabola. k and ε increase towards the wall, consistent with shear production. Symmetry about the axis is preserved.
IMPLICATION
The solution is physically consistent before any comparison with measured data.

## Slide 14
I · INTERNAL FLOW · CFD
14
Inner scaling: the profile crosses the logarithmic range
SCALING
uτ = (τw/ρ)1/2, y+ = y uτ/ν, W+ = W/uτ . Compared with viscous and logarithmic laws.
Friction velocity
0.03654 m/s
Maximum plotted y+
≈ 1699
OBSERVATION
The computed profile follows the logarithmic law over the resolved range.
SCOPE
Maximum y+ is the wall-to-axis distance. The near-wall resolution cannot be reconstructed from the compact exports.

## Slide 15
I · INTERNAL FLOW · CFD
15
All four closures reproduce the measured profile shape
METHOD
CFD profiles interpolated to the experimental radial coordinates; normalised RMSE against two measured series at Reb = 75,000.
Model
Profile RMSE
Standard k–ε
0.0158
RNG k–ε
0.0166
Realisable k–ε
0.0195
Low-Re k–ε
0.0214
IMPLICATION
RMSE spans only 0.016–0.021: profile shape alone weakly discriminates between closures. Wall friction is needed.

## Slide 16
I · INTERNAL FLOW · CFD
16
Wall friction discriminates between the closures
References: experiment 0.0190 · Prandtl 0.01912 · Haaland 0.01895
Model
f
Error vs exp.
Standard k–ε
0.018984
0.082%
RNG k–ε
0.018403
3.14%
Realisable k–ε
0.017853
6.04%
Low-Re k–ε
0.021688
14.15%
INTERPRETATION
The low-Re closure overpredicts wall friction on this grid. Its sensitivity to near-wall resolution requires a dedicated refinement study.
Standard k–ε gives the smallest friction and profile errors for the grids and wall treatments tested.

## Slide 17
PART II
Cylinder wake experiment
Calibration of the measurement chain, then the wake through its velocity field, its forces and their uncertainty.
18 Experimental setup
19 Load-cell calibration
20 Calibration stability
21 Mean wake
22 Wake recovery
23 Probe spectrum
24 Vorticity phases
25 Cylinder forces
26 Lift spectrum
27 Uncertainty budget

## Slide 18
II · CYLINDER WAKE · EXPERIMENT
18
Experimental setup
Circular cylinder, D = 0.06 m, in a 0.50 m wide open channel.
Quantity
PSV
Forces
Flow rate
35 L/s
75 L/s
Water depth
0.42 m
0.45 m
Bulk velocity Ub
0.1667 m/s
0.3333 m/s
Sampling rate
50 Hz
200 Hz
Data
1499 fields, 23×30
span 0.185 m
PSV
Particle-shadow velocimetry: pixel displacements converted at 3040 px/m, local velocity field in the cylinder frame.
FORCES
Calibrated load cell: span-integrated drag and lift, buoyancy removed with a still-water record.

## Slide 19
II · CYLINDER WAKE · EXPERIMENT
19
Load cell: linear transfer function over −10.5 to 13.8 N
Sensitivity S
−4.078·10−4 V/N
R2
0.9999988
Force RMSE
0.00572 N
Max residual
0.01398 N
METHOD
Sixteen static loads at 100 Hz. Fit V = SF + V₀ using the last 30% of each record.
OBSERVATION
No sign-dependent slope or visible curvature. Largest residual near −0.41 N.
IMPLICATION
Small relative to mean drag (0.92 N), but comparable to mean lift (−0.017 N).

## Slide 20
II · CYLINDER WAKE · EXPERIMENT
20
Small loads need long records to settle
CRITERION
Cumulative mean within a 2% band of the final level.
Reference load
Settling time
0 N
25.99 s
|F| ≤ 0.41 N
11.9–21.0 s
|F| ≥ 0.70 N
≤ 0.49 s
OBSERVATION
High loads settle almost immediately; near zero, drift and noise are comparable with the signal.
IMPLICATION
Justifies the last-30% window and sets the practical limit for interpreting mean lift.

## Slide 21
II · CYLINDER WAKE · EXPERIMENT
21
Mean wake: velocity deficit bounded by separated shear layers
Reynolds number
ReD = 9980
Bulk velocity
0.1667 m/s
METHOD
Time average of 1499 PSV fields. Invalid vectors omitted, cylinder interior masked, no spatial interpolation.
OBSERVATION
Streamwise velocity drops behind the cylinder and a deficit forms around the centreline. Vectors show transverse motion from the shear layers.
SCOPE
Boundary regions with few valid vectors are not interpreted.

## Slide 22
II · CYLINDER WAKE · EXPERIMENT
22
Streamwise recovery of the mean velocity
METHOD
Vertical profiles of mean streamwise velocity at four downstream stations.
OBSERVATION
The strongest deficit and cross-stream variation occur in the near wake. Profiles smooth out downstream as momentum is redistributed.
SCOPE
The field of view is too short to establish a self-similar far-wake regime.

## Slide 23
II · CYLINDER WAKE · EXPERIMENT
23
Velocity spectrum: one dominant frequency, St = 0.204
METHOD
Transverse velocity at the valid grid point nearest to
(x/D, y/D) = (0.25, 0), i.e. (0.288, −0.057). Gaps interpolated in time; peak searched in 0.2–10 Hz.
Dominant frequency
0.567 Hz
St = fsD/Ub
0.204
OBSERVATION
A single peak well above the broadband level over a 30 s record at 50 Hz.
IMPLICATION
Consistent with periodic shedding behind a circular cylinder at ReD ≈ 104.

## Slide 24
II · CYLINDER WAKE · EXPERIMENT
24
Vorticity phases: alternating vortices convected downstream
METHOD
Four frames separated by a quarter of the identified period, from a moving-average filtered sequence.
OBSERVATION
Alternating signed structures form behind the cylinder and are convected through the measurement region.
IMPLICATION
Spatial counterpart of the spectral peak. Topology only: no ensemble phase average, amplitudes not interpreted.

## Slide 25
II · CYLINDER WAKE · EXPERIMENT
25
Mean drag coefficient 1.50; mean lift close to zero
METHOD
C = F / (½ρUb2DL), L = 0.185 m. Lift corrected for buoyancy with the still-water record.
Mean drag
0.9223 N
Mean lift
−0.0172 N
C̅D
1.4987
C̅L
−0.0280
OBSERVATION
Drag fluctuates about a positive mean; lift oscillates about zero.
IMPLICATION
A non-zero mean lift alone is not evidence of physical asymmetry.

## Slide 26
II · CYLINDER WAKE · EXPERIMENT
26
Lift spectrum: shedding at St = 0.181
METHOD
One-sided amplitude spectrum of the corrected lift after mean removal, 200 Hz.
WHY LIFT
Alternating shedding forces the cylinder cross-stream at fs ; drag responds mainly at the mean and at even harmonics.
Shedding frequency
1.006 Hz
St
0.181
IMPLICATION
The narrow peak indicates a coherent periodic component, measured independently of the velocity field.

## Slide 27
II · CYLINDER WAKE · EXPERIMENT
27
Force measurement dominates the uncertainty budget
METHOD
First-order propagation, root sum of squares of independent contributions (assumptions in appendix A2).
u(CD)
0.0756 · 5.0%
u(CL)
0.0574
2 mm level mismatch
ΔCL ≈ 0.0229
OBSERVATION
Force measurement dominates both coefficients. Velocity is next for drag, since C ∝ Ub−2.
The mean lift is smaller than its uncertainty: it is compatible with zero.

## Slide 28
SYNTHESIS
What the evidence supports
Cross-comparison of independent estimates, conclusions and the range over which they hold.
29 Strouhal comparison
30 Conclusions
31 Range of validity and extensions

## Slide 29
SYNTHESIS
29
Two Strouhal estimates, one shedding regime
PSV · LOCAL VELOCITY
0.204
fs = 0.567 Hz at Ub = 0.167 m/s
LOAD CELL · LIFT
0.181
fs = 1.006 Hz at Ub = 0.333 m/s
|ΔSt| = 0.023, force estimate 11.3% below PSV
DIFFERENCES BETWEEN THE ACQUISITIONS
1
Bulk velocity doubles between the two acquisitions.
2
Water depth changes from 0.42 to 0.45 m.
3
The estimators differ: local transverse velocity against span-integrated force.
Both estimates indicate the same shedding regime, but the tests were conducted under different flow conditions.

## Slide 30
SYNTHESIS
30
Conclusions
1
LAMINAR CFD · VERIFIED
Final refinement changes the observables by less than 1%. Profile error 3.18%, pressure-gradient error 1.24%.
2
TURBULENT CFD · VALIDATED
Standard k–ε gives the lowest profile RMSE and f = 0.018984, 0.082% from experiment.
3
MEASUREMENT CHAIN
Linear load cell, R2 = 0.9999988. Near-zero loads settle slowly and bound the interpretation of mean lift.
4
CYLINDER WAKE
C̅D = 1.499 ± 0.076, C̅L = −0.028 ± 0.057. Coherent shedding at St = 0.181–0.204.
Each result is stated together with its reference, its error and the conditions under which it holds.

## Slide 31
SYNTHESIS
31
Range of validity and extensions
CONDITIONS OF THE RESULTS
Grid
Sensitivity quantified pairwise, below 1% on the final refinement in both regimes
Closures
Model ranking established for the implemented mesh and wall treatment
Wake field
Mean field and shedding frequency quantitative; vorticity phases describe topology
Forces
Instrument-chain uncertainty propagated; installation effects bounded by a level-mismatch scenario
Strouhal
Two operating points, compared through nondimensional quantities
EXTENSION · OUTCOME
Constant-ratio grid triplets
→
GCI and extrapolated solution
First-cell y+ control
→
Targeted assessment of the low-Re wall treatment
Conditional phase averaging
→
Quantitative vortex strength
Blockage and free-surface corrections
→
Unbounded-flow force coefficients
Synchronous PSV and force acquisition
→
Direct Strouhal cross-validation at one operating point
The same verification and validation chain extends directly to each case.

## Slide 32
APPENDIX
Supporting material
Complete grid-sensitivity metrics and the assumptions behind the uncertainty budget.
A1 Grid metrics
A2 Uncertainty assumptions

## Slide 33
APPENDIX
A1
Complete grid-sensitivity metrics
Regime
Refinement
Coarse–medium
Medium–fine
Laminar
Radial
2.359%
0.521%
Axial
0.412%
0.225%
Combined
1.438%
0.925%
Turbulent
Radial
0.842%
0.242%
Axial
0.260%
0.132%
Combined
0.625%
0.366%
Relative L∞ difference between successive grids. Pairwise differences, not an asymptotic GCI.

## Slide 34
APPENDIX
A2
Uncertainty assumptions and limitations
PROPAGATED · FIRST ORDER
Drag force
0.045 N
Each vertical contribution
0.025 N
Depth, channel width
1 mm
Cylinder diameter
0.05 mm
Span
1 mm
Flow rate
0.5% + meter head
NOT PROPAGATED
Blockage
Free-surface deformation
End effects
Alignment
Non-simultaneous PSV and force acquisitions